BOB SCOTT B.Sc. C.Eng. M.I.Struct.E.

Consulting Structural Engineer

Unit 2, Barnwell Manor Ind. Estate, Home Farm, Barnwell, PETERBOROUGH, PE8 5PL			Tel/Fax: (01832) 274604

E-mail: scott.robert@btconnect.com

Your Ref:

Drawing Ref: 06007/01

Bending Schedule Sheet				Date: January 2006

Sheet Ref: 06007/BS1

Job Ref: Proposed New Boathouse, Barnwell

| Member | Bar mark | Type and size | No of mbrs | No of bars in each | Total no. | Length of each bar † mm | ShapeCode | A* mm | B* mm | C* mm | D* mm | E/R* mm | Rev letter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Reinforced Raft | 01 | D16 | 24 | 1 | 24 | 4775 | 00 |  |  |  |  |  |  |
|  | 02 | D12 | 12 | 1 | 12 | 4775 | 00 |  |  |  |  |  |  |
|  | 03 | D16 | 24 | 1 | 24 | 4950 | 00 |  |  |  |  |  |  |
|  | 04 | D12 | 12 | 1 | 12 | 4950 | 00 |  |  |  |  |  |  |
|  | 05 | D16 | 60 | 1 | 60 | 3475 | 00 |  |  |  |  |  |  |
|  | 06 | D12 | 12 | 1 | 12 | 3475 | 00 |  |  |  |  |  |  |
|  | 07 | D12 | 18 | 1 | 18 | 1450 | 00 |  |  |  |  |  |  |
|  | 08 | D16 | 36 | 1 | 36 | 1750 | 00 |  |  |  |  |  |  |
|  | 09 | D12 | 6 | 1 | 6 | 1350 | 00 |  |  |  |  |  |  |
|  | 10 | D16 | 30 | 1 | 30 | 1650 | 00 |  |  |  |  |  |  |
|  | 11 | D10 | 224 | 1 | 224 | 1275 | 51 | 190 | 370 | 125 |  |  |  |
|  | 12 | D10 | 224 | 1 | 224 | 1525 | 51 | 540 | 145 | 125 |  |  |  |
|  | 13 | D10 | 90 | 1 | 90 | 1725 | 51 | 415 | 370 | 125 |  |  |  |
|  | 14 | D16 | 20 | 1 | 20 | 1975 | 21 | 860 | 315 | 860 |  |  |  |
|  | 15 | D16 | 8 | 1 | 8 | 1950 | 21 | 860 | 385 | 860 |  |  |  |
|  | 16 | D10 | 90 | 1 | 90 | 1400 | 00 |  |  |  |  |  |  |
|  | 17 | D10 | 164 | 1 | 164 | 1225 | 11 | 200 | 1035 |  |  |  |  |
|  | 18 | D10 | 60 | 1 | 60 | 800 | 11 | 200 | 610 |  |  |  |  |
|  |  | A393 Mesh | 12 | 1 | 12 |  |  |  |  |  |  |  |  |

This schedule complies with BS 8666-2000

* Specified in multiples of 5mm.

† Specifed in multiples of 25mm.